## Slide 1
Mapping:
Data Transport
Jered McClure
Walden University
Notes: Mapping: Data Transport
Jered McClure
Walden University

## Slide 2
Input Keyboard/Mouse Write the email message, or request email message.
Local Router/ Modem Routes data from the correct computer to the DSLAM, headers attached.
DSLAM Digital Subscriber Line Access Multiplexer. Each DSL signal is filtered and routed to the correct ISP.
ISP/SMTP The ISP sends the email to an SMTP server which pulls the address out of the message and sends it to the DNS, once an address is found it sends it to the destination SMTP server.
Regional Routers/Backhaul Providers Packets are routed to the correct destination.
Firewall Packets are checked against filters for access, both upwards and downwards, on the stack.
Location Router/Modem Router confirms packet retrieval and strips header.
Firewall Packets are checked against filters for access, both upwards and downwards, on the stack.
SMTP/POP/IMAP Server/Computer Server determines email message location, stores it and/or sends it back up the stack to further locations.
Encapsulation Email is encapsulated using SMTP into packets, or packet request sent via POP3/IMAP.
De-encapsulation Packets are De-encapsulated. Headers stripped, and message retrieved.
Computer Data storage, manipulation, & retrieval. Store and retrieve the email application software.
ISP/DNS The DNS gets the IP address of the destination email server and sends it back to the SMTP Server.
Note: There may be additional DSLAMs, and routers, before reaching destination.
Email Message Sending and/or Receiving
Notes: Computer: Stores data on a hard drive. Retrieves data from the HDD to the RAM. Manipulates data in the RAM.
Encapsulation: “The process of passing data down the stack using PDUs” (Doherty, Anderson, Maggiora, & Clement, 2008).
De-Encapsulation: “the process of passing information up the stack” (Doherty, Anderson, Maggiora, & Clement, 2008, P. 9).
Firewall: Software on the router and/or computer used to block unwanted traffic, and/or “destructive forces” from reaching a destination (Tyson, 2000).
Local Router/Modem: ADSL2+ 2701HGV-W Gateway Modem/Router.
DSLAM: Location, Howrah Tasmania Exchange.
ISP: Telstra Bigpond Internet ADSL2+ 200GB (Telstra, 2011).
Regional Routers: E.g. Cisco Carrier Routing system (Cisco, 2011).
SMTP: Simple Mail transfer Protocol (Doherty, Anderson, Maggiora, & Clement, 2008, P. 28).
IMAP: Internet Message Access Protocol (Doherty, Anderson, Maggiora, & Clement, 2008, P. 28).
POP: Also known as POP3, Post Office Protocol (Doherty, Anderson, Maggiora, & Clement, 2008, P. 28).
SMTP sends emails, where as, IMAP and POP3 retrieve emails. SMTP cannot retrieve emails.

## Slide 3
Streaming Data to a Wireless Device
Wireless Device User inputs a request for a video stream.
Wireless Router Receives encrypted packet, decrypts with appropriate WPA keys and strips headers.
Firewall Packets are checked against filters for access, both upwards and downwards, on the stack.
Computer/Server Reads message and acknowledges receipt by sending video stream.
Encapsulation Stream is encapsulated into packets and sent to the router.
Firewall Packets are checked against filters for access, both upwards and downwards, on the stack.
Wireless Router The router places headers on the packets then broadcasts then via WPA encrypted Wi-Fi Omni-directionally.
De-Encapsulation Packets are stripped of headers and de-encapsulated
Encapsulation Wireless device encapsulates request in packets with headers and encrypts with WPA. Then sends the packet via Wi-Fi to the router.
De-Encapsulation The wireless device receives the broadcast, decrypts the packets, strips the headers, and plays the video stream.
Notes: Wireless Device: A device which transmits and/or receives wireless signals such as Wi-Fi (802.11 *) or Bluetooth (E.g. an iPhone or Android phone with wireless capability).
Encapsulation: “The process of passing data down the stack using PDUs” (Doherty, Anderson, Maggiora, & Clement, 2008, P. 9).
WPA: Also known as WPA2, which stands for “Wi-Fi Protected Access 2,” is an encryption standard used to keep wireless networks private (Doherty, Anderson, Maggiora, & Clement, 2008, P. 100).
Wireless Router: ADSL2+ 2701HGV-W Gateway Modem/Router.
Firewall: Software on the router and/or computer used to block unwanted traffic, and/or “destructive forces” from reaching a destination (Tyson, 2000).
De-Encapsulation: “the process of passing information up the stack” (Doherty, Anderson, Maggiora, & Clement, 2008, P. 9).
Computer/Server: This can be any device

## Slide 4
References
Cisco. (2011). Cisco Carrier Routing System. Retrieved October 7, 2011, from Cisco Systems: http://www.cisco.com/en/US/products/ps5763/index.html
Doherty, J., Anderson, N., Maggiora, P. D., & Clement, N. (2008). Cisco Networking Simplified (2nd ed.). Indianapolis: Cisco Press.
Telstra. (2011). BigPond Elite 200GB. Retrieved October 7, 2011, from Telstra Bigpond: http://go.bigpond.com/broadband/69-plan/
Tyson, J. (2000, October 24). How Firewalls Work. Retrieved October 07, 2011, from How Stuff Works: http://www.howstuffworks.com/firewall.htm
Notes: References
Cisco. (2011). Cisco Carrier Routing System. Retrieved October 7, 2011, from Cisco Systems: http://www.cisco.com/en/US/products/ps5763/index.html
Doherty, J., Anderson, N., Maggiora, P. D., & Clement, N. (2008). Cisco Networking Simplified (2nd ed.). Indianapolis: Cisco Press.
Telstra. (2011). BigPond Elite 200GB. Retrieved October 7, 2011, from Telstra Bigpond: http://go.bigpond.com/broadband/69-plan/
Tyson, J. (2000, October 24). How Firewalls Work. Retrieved October 07, 2011, from How Stuff Works: http://www.howstuffworks.com/firewall.htm